## Slide 1: Introduction to "ivy"
Block storage synthetic workload generator with real time dynamic feedback control
Hitachi Data Systems
2016-05-16
Allart Ian Vogelesang ian.vogelesang@hds.com +1 408 396 6511

## Slide 2: Why ivy?
Reduce cost
Speed time to market
Improve quality
Simplify test setup
Measure IOPS at a specified response time (dynamic feedback control)
Get trust in measurement results through open source

## Slide 3: ivy in one chart
Written in C++ using Linux native kernel Asynchronous I/O interface
  Lowest CPU overhead – minimizes test host hardware cost & maximizes measurement accuracy
  Designed for open source / vendor independence, with a separately packaged Hitachi proprietary component.
Super easy test setup – select by LDEV, by Port, by PG, Pool ID (by drive type with command device)
Can test for minimum time necessary to make a valid measurement to a specified +/- accuracy
Real-time dynamic feedback control (DFC) enables for the first time to
  "measure IOPS at 1 ms service time" (using DFC on rolled up host workload data – any vendor's equipment)
  "measure IOPS at 50% owning MP core % busy" (using DFC on filtered & rolled up command device data)
Records subsystem command device performance data synchronized with host workload data
  Makes validating / calibrating models easier
Records only valid measurement data
  Checks number of resources reporting (ports, PGs, LDEVs, etc.) and that none running too slowly. Checks that subsystem does not have any failed components (with command device).
Enables workflow automation using ivyscript programming language wrapper around ivy engine.
Items in italics only available to authorized Hitachi internal users using command device connector and license key

## Slide 4: Scalable
In ivy, you can layer multiple named “workload” I/O generator threads on LUNs
Each workload thread uses an I/O sequencer plug-in that generates I/Os in scheduled I/O start time sequence.
  We try to keep a few I/Os “pre-computed” and ready to go at all times.
  Generalized interface allows use of any I/O pattern generator, e.g. synthetic or playback.
Use of C++ with Linux kernel Asynchronous I/O interface means each workload thread can drive any queue depth up to limits of the OS / HBA with state of the art minimal CPU overhead.
testhost1
OS
LUN
HBA
LUN
LUN
HBA
LUN
Ivyslave main thread
Workload
Workload
Workload
Workload
Workload
Workload
Workload
Workload
Workload
NIC
Workload
Workload
Workload
by-host subthread
NIC
testhost2
OS
LUN
HBA
Workload
Workload
Workload
by host subthread
by host subthread
ivy master host
Ivy main thread
[hosts] statement
[CreateWorkload] statement

## Slide 5: ivy – designed for vendor independence
Vendor proprietary simple SCSI Inquiry-based LUN discovery tool
  Vendor's attribute names / values become selectable in ivy.
  Hitachi LUN discovery tool is open source - https://github.com/Hitachi-Data-Systems/LUN_discovery
Ivy
  Open source - https://github.com/Hitachi-Data-Systems/ivy
  HDS Community site - https://community.hds.com/groups/ivy
    (Send Ian an email to get an invitation to join, but will be public very soon.)
For authorized internal Hitachi users with code and license key - vendor proprietary "connector" to retrieve real time storage product configuration and/or performance data
  Enables ivy dynamic feedback control on internal storage metrics.

## Slide 6: ivy - open source / vendor independent
To support any vendor's architecture and terminology in ivy, all you need is a LUN discovery tool that makes a csv file with
  a header line that defines vendor-specific attribute names, and
  a data line for each LUN decoding that LUN attributes.
Hitachi's LUN_discovery tool set using "showluns.sh" script produces something like this:
      host,LUN name,HDS product,port,LDEV,PG,CLPR, … testy1,/dev/sdxy,VSP,1A,00:00,1-1,CLPR0, … testy2,/dev/sdyz,VSP,2A,00:01,1-2,CLPR0, …

## Slide 7: Functionality expands with proprietary connector
Vendors are encouraged to prepare their own proprietary "subsystem connector" interface tools to be used with ivy.
  Collect subsystem configuration data to augment SCSI Inquiry attribute data
    Select a test configuration based on attributes such as disk drive type.
  Collect real time subsystem performance data, synchronized and aligned with test host workload data.
    Facilitates development of modeling tools.
  Use dynamic feedback control to find the IOPS to reach a target value for
    subsystem MP % busy, or
    drive % busy, or
    cache dirty data % full, etc.

## Slide 8: Hitachi's proprietary connector does all those things
Hitachi's "ivy command device connector" (ivy_cmddev) is not part of the ivy open source project and will remain proprietary for internal Hitachi R&D use.
  "command device" based functionality is not available to the public.
Ivy presentation material and sample demo output & videos describe Hitachi command device connector functionality so as to
  Show what ivy was designed to do
  Serve to illustrate the functionality that other vendors could achieve by developing their own connectors.

## Slide 9: [hosts] statement – configuration discovery
master host
testhost3
ivyslave executable
testhost2
ivyslave executable
command line: ivy test2
[hosts] "testhost1" to "testhost3"
test2.ivyscript
ivy executable
testhost1
ivyslave executable
showluns.sh executable
Host,LUN,HDS Product,LDEV,PG testhost1,/dev/sdxy,VSP,00:00,1-1
Host,LUN,HDS Product,LDEV,PG testhost1,/dev/sdxy,VSP,00:00,1-1
testhost2,/dev/sdxy,VSP,00:01,1-2
testhost3,/dev/sdxy,VSP,00:02,1-3
csv column headings become selectable in ivy
Separate vendor-proprietary SCSI Inquiry tool outputs csv file decoding storage LUN attribute names & values

## Slide 10: [CreateRollup] "LDEV";
A rollup is what mathematicians call a "partition" – a way to divide a collection of things (in this case host-LUN-workload threads) into subgroups.
There is by default always a rollup called "all" which has one rollup instance, also called "all" which consists of all workloads on all LUNs on all hosts.
Otherwise, a rollup name must be combination of LUN attribute names
If you have multiple subsystems under test, to get data rolled up by subsystem by port say [CreateRollup] "serial_number+port"; and get instances like "410034+1A".

## Slide 11: Rollups are multi-purpose
The default is to print csv files by rollup instance.
  Say [nocsv] to suppress.
On the [Go] statement to run a subinterval sequence, focus_rollup="PG"
  Both dfc=pid, the dynamic feedback control feature, as well as measure=on, the "seen enough and stop" [Go] statement feature operate at the granularity of the rollup instance.
[CreateRollup] "port" [quantity] 32;
  Will invalidate measurements if we don't get data for exactly 32 subsystem ports.
[CreateRollup] "port" [MaxDroop] "20%";
  Invalidates if there is a port whose IOPS is more than 20% slower than the fastest port.

## Slide 12: ivy dynamic feedback control (DFC)
Subinterval n-1
Subinterval n
Collect & rollup test host workload data (fraction of a second)
Subinterval n+1
Subinterval n+2
With DFC=PID, workload parameter updates (usually "IOPS=xxx") sent out and applied in real time to workload I/O sequencer. Does not affect I/Os in "precompute Q, ready to launch".
cmd dev subinterval may not exactly align, but offset is minimal
cmd dev gather timed so data arrive centrally just in time at end of subinterval
typically 5 seconds

## Slide 13: industry standard "PID Loop" controller
Chart: Subinterval number
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.250_x_baseline
1.250_x_baseline
Target service time
ivyscript automated workflow:
Measure max IOPS
Measure "baseline" service time at 1% of max IOPS
Use PID loop dynamic feedback control to measure IOPS for various multiples of baseline service time

## Slide 14: measure=on, cooldown_by_wp=on
Chart: Seconds
Warmup IOPS | 34402 | 42682 | 46147 | 46135 | 46197 | 47208 | 9018 | 1836 | 802 | 8209 | 7929 | 213 | 10891 | 7723 | 2722 | 3181 | 3093 | 3856 | 2838 | 2084 | 2792 | 1881 | 3806 | 1846 | 3366 | 1522 | 3570 | 1212 | 7204 | 1245 | 2136 | 1484 | 2546 | 1447 | 2737 | 1667 | 2153 | 849 | 880 | 752 | 781
Measurement IOPS | 888 | 909 | 1085 | 832 | 906 | 1123 | 973 | 959 | 920 | 1070 | 1045 | 943 | 1083 | 954 | 1027 | 1130 | 1141 | 1081 | 1106 | 896 | 1028 | 1105 | 887 | 1037 | 874 | 959 | 936 | 782 | 1034 | 949 | 949 | 932 | 902 | 884 | 986 | 876
Stable measurement period identified by algorithm
Initial transient behaviour
“cooldown_by_wp = on” extends until WP is empty.
(WP data from cmd dev.)
Without a command device, stable measurement identification can be effective but can take a little longer

## Slide 15: DFC on command device connector data
Chart: For parity group busy % = 10%, 20%, 30%, …
| 9.950800000000011E-2 | 0.19962099999999997 | 0.29997200000000035 | 0.40008000000000027 | 0.50149100000000002 | 0.60100600000000004 | 0.70207500000000045 | 0.80312099999999997 | 0.90364599999999995 | 0.95612600000000003 | 0.99374700000000005
 | 3612.13 | 7680.14 | 11794.7 | 17398.6 | 23119.2 | 30544.7 | 39590.5 | 52291.5 | 74647.2 | 98869.1 | 153015
Actually achieved PG busy %

## Slide 16: Fine-grained dynamic feedback control
Chart: 
| 10% busy | 20% busy | 30% busy | 40% busy
MPU0 | 12574.6 | 26557.2 | 42388.2 | 57959.5
MPU1 | 9852.86 | 20783.7 | 33109.1 | 45796.2
MPU2 | 11482.2 | 25159 | 40517.9 | 55810.4
MPU3 | 9474.12 | 20309.9 | 32416.3 | 44996.2
[CreateRollup] "MPU";
[Go!] "DFC=PID, focus_rollup=\"MPU\" …"
IOPS

## Slide 17: DFC on host workload data – non proprietary
Chart: IOPS
| 39.945800000000006 | 1501.84 | 1917.41 | 2417.1999999999998 | 2730.61 | 2965.8900000000012 | 3277.04 | 3321.94 | 3355.4900000000002 | 3376.55
 | 6.5622 | 6.9609 | 7.8127 | 9.49 | 11.1534 | 12.8037 | 16.1068 | 19.3879 | 25.9613 | 32.5304
ivyscript automated workflow:
Measure max IOPS (not shown)
Measure "baseline" service time at 1% of max IOPS
Use PID loop dynamic feedback control to measure IOPS for various multiples of baseline service time

## Slide 18: Service time histograms
Chart: Read Service Time at 90% of max IOPS
| 0.0x | 0.1x | 0.2x | 0.3x | 0.4x | 0.5x | 0.6x | 0.7x | 0.8x | 0.9x | 1.x | 2.x | 3.x | 4.x | 5.x | 6.x | 7.x | 8.x | 9.x | 10.x | 11.x | 12.x | 13.x | 14.x | 15.x | 16.x | 17.x | 18.x | 19.x | 2x. | 3x. | 4x. | 5x. | 6x. | 7x. | 8x. | 9x. | 1xx. | 2xx. | 3xx. | 4xx. | 5xx. | 6xx. | 7xx. | 8xx. | 9xx. | 1xxx. | 2xxx. | 3xxx. | 4xxx. | 5xxx. | 6xxx. | 7xxx. | 8xxx. | 9xxx. | 10000+
90% of max IOPS 100% read | 0.33 | 0.073333 | 0.0066667 | 0.0033333 | 0.0066667 | 1.07 | 11.8433 | 42.4867 | 85.5067 | 120.58 | 134.537 | 129.66 | 112.63 | 98.2333 | 87.17 | 73.7767 | 63.5733 | 55.0167 | 49.4233 | 43.66 | 38.8767 | 33.6067 | 31.0333 | 28.2633 | 169.49 | 70.3267 | 31.1833 | 14.57 | 7.3933 | 3.9867 | 1.9867 | 1.1033 | 1.4033 | 0.0066667
90% of max IOPS 75% read | 0.17209 | 0.054016 | 0.012048 | 0.0072289 | 0.0086345 | 0.0040161 | 0.0040161 | 0.0050201 | 0.0032129 | 0.38133 | 4.458 | 16.9014 | 34.7841 | 50.401 | 59.4129 | 61.2412 | 58.6414 | 55.2402 | 52.0253 | 48.0966 | 43.1629 | 38.3028 | 34.3253 | 30.3819 | 26.7347 | 23.8488 | 21.912 | 20.0799 | 133.534 | 69.7528 | 41.6735 | 27.49 | 18.756 | 13.254 | 9.4034 | 6.7781 | 17.851 | 1.206 | 0.11165 | 0.01245 | 0.0012048 | 0.0002008
90% of max IOPS 50% read | 0.14984 | 0.041042 | 0.0013029 | 0.0019544 | 0.0013029 | 0.00065147 | 0.25668 | 3.3974 | 12.0319 | 22.2313 | 30.1824 | 33.0762 | 31.5713 | 28.9596 | 27.1954 | 25.542 | 23.0873 | 20.6756 | 18.4365 | 16.7016 | 15.058 | 13.7687 | 12.7752 | 12.0072 | 11.1062 | 83.6156 | 49.8358 | 32.3433 | 22.129 | 15.5837 | 11.2899 | 8.1062 | 5.8234 | 15.602 | 1.0143 | 0.10749 | 0.011075 | 0.0019544 | 0.00065147
90% of max IOPS 25% read | 0.063535 | 0.029978 | 0.00022371 | 0.00022371 | 0.00022371 | 0.11723 | 1.6479 | 5.5586 | 10.1076 | 13.4311 | 14.6676 | 13.8065 | 12.4065 | 11.3633 | 10.3899 | 9.2723 | 8.1962 | 7.3461 | 6.7763 | 6.2924 | 5.9931 | 5.6796 | 5.4711 | 5.2074 | 41.3841 | 24.8418 | 14.9168 | 9.8926 | 6.8058 | 4.9157 | 3.5902 | 2.7982 | 9.317 | 1.0611 | 0.17673 | 0.029083 | 0.0071588 | 0.0011186 | 0.00044743 | 0.00022371
90% of max IOPS 0% read
Chart: Write Service Time at 90% of max IOPS
| 0.0x | 0.1x | 0.2x | 0.3x | 0.4x | 0.5x | 0.6x | 0.7x | 0.8x | 0.9x | 1.x | 2.x | 3.x | 4.x | 5.x | 6.x | 7.x | 8.x | 9.x | 10.x | 11.x | 12.x | 13.x | 14.x | 15.x | 16.x | 17.x | 18.x | 19.x | 2x. | 3x. | 4x. | 5x. | 6x. | 7x. | 8x. | 9x. | 1xx. | 2xx. | 3xx. | 4xx. | 5xx. | 6xx. | 7xx. | 8xx. | 9xx. | 1xxx. | 2xxx. | 3xxx. | 4xxx. | 5xxx. | 6xxx. | 7xxx. | 8xxx. | 9xxx. | 10000+
90% of max IOPS 100% read
90% of max IOPS 75% read | 47.4494 | 179.16 | 11.5934 | 9.2586 | 7.1843 | 5.0932 | 4.5394 | 4.3038 | 4.1203 | 33.9386 | 19.9825 | 8.7104 | 3.2034 | 0.89197 | 0.31245 | 0.11526 | 0.047189 | 0.016667 | 0.0054217 | 0.0034136 | 0.001004 | 0.0002008 | 0.0002008
90% of max IOPS 50% read | 101.851 | 476.814 | 12.8345 | 2.3127 | 1.63 | 1.1107 | 0.85994 | 0.62997 | 0.47622 | 3.2072 | 0.9114 | 0.36482 | 0.19935 | 0.087296 | 0.057329 | 0.033225 | 0.014332 | 0.009772 | 0.0065147 | 0.0052117 | 0.0045603 | 0.0026059 | 0.0026059 | 0.0013029 | 0.00065147 | 0.00065147 | 0.0032573 | 0.0032573 | 0.0039088
90% of max IOPS 25% read | 112.717 | 674.049 | 16.9043 | 2.7485 | 1.7251 | 1.2944 | 1.0412 | 0.75839 | 0.62595 | 3.7626 | 1.2631 | 0.83535 | 0.62327 | 0.46197 | 0.3519 | 0.28971 | 0.21342 | 0.16644 | 0.13356 | 0.10447 | 0.083893 | 0.070694 | 0.05906 | 0.043624 | 0.035794 | 0.030649 | 0.025503 | 0.02528 | 0.11767 | 0.040268 | 0.0217 | 0.014541 | 0.012528 | 0.00783 | 0.006264 | 0.0049217 | 0.028412 | 0.0051454
90% of max IOPS 0% read | 788.3 | 217.327 | 6.7667 | 2.2833 | 1.3567 | 1.0033 | 0.81667 | 0.65333 | 0.62667 | 2.84 | 0.20333 | 0.01

## Slide 19: Workloads can be placed within the LUN
Chart: Sequential MB/s by zone

## Slide 20: Ivy development status
May, 2016 initial version.
  Ready for initial use by Hitachi internally
  Approved for release as open source release. Now preparing HDS community site for opening for public access by end of May.
  Demos available for all functionality.
  No official QA performed (developer testing only), no end user experience yet.
  Support for VSP Gx00, most, but not all command device data.
  Support for HUS100 series.

## Slide 21: Ivy futures
Need "shakedown" user experience before layering more development
Dedupe / compression features – in development
Some ideas for the future:
  Repackage access to ivy engine via a RESTful API.
    Build CLI on RESTful API to enable programming ivy in Python or any other language
    Remove outer ivyscript programming layer wrapper, exposing ivy engine control statements as CLI commands.
  Develop VSP G1000 support
  Extend VSP Gx00 support
  Develop "auto gain control" feature for PID loop
  Transition to POSIX asynchronous I/O and port to other OS platforms.

## Slide 22: Thank You