## Slide 1: Testing in minimum time with ivy "seen enough & stop"
April 4, 2016 Allart Ian Vogelesang ian.vogelesang@hds.com +1 408 396 6511

## Slide 2: What does it mean – a “valid” measurement
Valid results are repeatable
  If you run the test again, within specified +/- experimental error, you will get the same result again.
  Valid, repeatable, results are for steady-state, sustainable conditions
If the workload / subsystem are not steady-state, you can’t make a valid measurement.
  After imposing a workload on the subsystem, we need to wait for the behaviour to settle down into a steady state before we start measuring

## Slide 3: [Go] statement measure=on is "seen enough & stop"
measure = on
accuracy_plus_minus = "5%"
  Default is "5%".
confidence = "95%"
  How confident you need to be that your measurement falls within the specified plus or minus range around the long term average that you would get measuring forever.
  Default is "95%"
  Ivy has a menu of 11 specific pre-loaded confidence values that you pick from.
    50%, 60%, 70%, 80%, 90%, 95%, 98%, 99%, 99.5%, 99.8%, and 99.9%
    http://en.wikipedia.org/wiki/Student%27s_t-distribution

## Slide 4: Standard statistical formulas need a tweak
The standard formulas are for when you want to estimate what the mean (average) measurement would be if you sampled across the entire population, a huge number of samples.
With the standard formulas, a set of samples is taken, each sample a random sample, meaning the selection of each sample is at random, unrelated to how any other sample was collected.
In ivy, we are sampling consecutive subintervals, and there is a correlation from subinterval to subinterval.
So my rough observation from running ivy a few times is to specify accuracy_plus_minus twice as tightely, e.g. say +/- 1 % to get +/- 2% accuracy

## Slide 5: Detecting stability – by observing only IOPS/service time
Chart: Seconds
Warmup IOPS | 34402 | 42682 | 46147 | 46135 | 46197 | 47208 | 9018 | 1836 | 802 | 8209 | 7929 | 213 | 10891 | 7723 | 2722 | 3181 | 3093 | 3856 | 2838 | 2084 | 2792 | 1881 | 3806 | 1846 | 3366 | 1522 | 3570 | 1212 | 7204 | 1245 | 2136 | 1484 | 2546 | 1447 | 2737 | 1667 | 2153 | 849 | 880 | 752 | 781
Measurement IOPS | 888 | 909 | 1085 | 832 | 906 | 1123 | 973 | 959 | 920 | 1070 | 1045 | 943 | 1083 | 954 | 1027 | 1130 | 1141 | 1081 | 1106 | 896 | 1028 | 1105 | 887 | 1037 | 874 | 959 | 936 | 782 | 1034 | 949 | 949 | 932 | 902 | 884 | 986 | 876
Stable measurement period identified by algorithm
Initial transient behaviour
“cooldown_by_wp = on” extends cooldown period until WP is empty. (This feature only with command device connector.)
In this example, the level of dirty data in cache (Write Pending %) was not used in the algorithm to detect stability. Thus this would work for any vendor's equipment. Later we will show a feature that does let you use WP in detecting a stable measurement period.

## Slide 6: Even without command device, algorithm is effective
Chart: Seconds
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34
warmup IOPS | 40077.5 | 44643 | 17923
Measure IOPS | 816.5 | 101 | 105 | 1024.5 | 1644.5 | 3062 | 2800 | 2724 | 2199.5 | 3609.5 | 2418.5 | 3069 | 2858.5 | 2785.5 | 3369.5
WP | 0.13 | 0.29 | 0.38 | 0.44 | 0.42 | 0.39 | 0.37 | 0.38 | 0.43 | 0.52 | 0.58 | 0.63 | 0.67 | 0.67 | 0.66 | 0.65 | 0.67 | 0.64
Chart: Seconds
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40
Warmup IOPS | 38783.5 | 40544.5 | 23901.5 | 1050 | 441.5 | 782.5
Measure IOPS | 1971.5 | 4927 | 2581 | 2293 | 2147.5 | 2442 | 2424.5 | 2006.5 | 2622 | 2852.5 | 2402.5 | 2693 | 2741.5 | 2530.5 | 2621
WP | 0.15 | 0.34 | 0.52 | 0.58 | 0.56 | 0.51 | 0.47 | 0.54 | 0.59 | 0.61 | 0.58 | 0.55 | 0.55 | 0.55 | 0.52 | 0.51 | 0.52 | 0.52 | 0.52 | 0.53 | 0.53
Chart: Seconds
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20 | 22 | 24 | 26 | 28 | 30 | 32 | 34 | 36 | 38 | 40 | 42 | 44 | 46 | 48 | 50 | 52 | 54 | 56 | 58 | 60 | 62 | 64 | 66 | 68 | 70 | 72 | 74 | 76 | 78 | 80 | 82 | 84 | 86 | 88 | 90 | 92 | 94 | 96 | 98 | 100 | 102 | 104 | 106 | 108 | 110
Warmup IOPS | 38859.5 | 44391.5 | 30524.5 | 1648.5 | 4247 | 2793 | 1080 | 1379.5 | 2087 | 3094 | 2109 | 1030.5 | 1958 | 4652.5 | 2631.5 | 4828 | 2823.5 | 3610 | 3299.5 | 4077.5 | 3951.5 | 2519 | 4514.5 | 3561 | 3523.5 | 3211 | 2458 | 2927.5 | 1849.5 | 2418.5 | 1819.5 | 2341 | 2336.5 | 2998 | 2125 | 3178.5 | 739.5 | 951.5 | 859.5 | 858 | 884
Measure IOPS | 906 | 978 | 838.5 | 944 | 961 | 994 | 970 | 1033 | 1003.5 | 949.5 | 1009.5 | 994 | 1042.5 | 969 | 894.5
WP | 0.23 | 0.48 | 0.65 | 0.66 | 0.66 | 0.68 | 0.61 | 0.57 | 0.53 | 0.62 | 0.59 | 0.56 | 0.52 | 0.56 | 0.6 | 0.66 | 0.68 | 0.68 | 0.66 | 0.66 | 0.66 | 0.64 | 0.67 | 0.62 | 0.63 | 0.63 | 0.63 | 0.64 | 0.65 | 0.65 | 0.65 | 0.67 | 0.68 | 0.69 | 0.68 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69 | 0.69
Accuracy +/- 20% Confidence 80%
Accuracy +/- 10% Confidence 80%
Accuracy +/- 2% Confidence 80%
Bogus measurement with loose criteria
WP shown for illustrative purposes, but is not being employed to detect stability in this case
Good measurement
Point at which Write Pending stabilizes
Bogus measurement with loose criteria
80% confidence only used to show algorithm failure. Normally we would use 95% confidence)

## Slide 7: Have not “seen enough”
Chart: Seconds
Warmup IOPS | 34402 | 42682 | 46147 | 46135 | 46197 | 47208 | 9018 | 1836 | 802 | 8209 | 7929 | 213 | 10891 | 7723 | 2722 | 3181 | 3093 | 3856 | 2838 | 2084 | 2792 | 1881 | 3806 | 1846 | 3366 | 1522 | 3570 | 1212 | 7204 | 1245 | 2136 | 1484 | 2546 | 1447 | 2737 | 1667 | 2153 | 849 | 880 | 752 | 781
Measurement IOPS | 888 | 909 | 1085 | 832 | 906 | 1123 | 973 | 959 | 920 | 1070 | 1045 | 943 | 1083 | 954 | 1027 | 1130 | 1141 | 1081 | 1106 | 896 | 1028 | 1105 | 887 | 1037 | 874 | 959 | 936 | 782 | 1034 | 949 | 949 | 932 | 902 | 884 | 986 | 876
At end of subinterval 65, when we looked back a short distance, we didn’t have enough subintervals to have “seen enough”
Looking back farther, we hit the unstable region – no match
Keep running more subintervals until we get an accuracy / confidence match, or if we time out.
After each subinterval completes, we “look back” at successively longer sub-sequences, each ending at the current subinterval, to see if they match the accuracy / confidence criteria

## Slide 8: “saw enough & stopped”
Chart: Seconds
Warmup IOPS | 34402 | 42682 | 46147 | 46135 | 46197 | 47208 | 9018 | 1836 | 802 | 8209 | 7929 | 213 | 10891 | 7723 | 2722 | 3181 | 3093 | 3856 | 2838 | 2084 | 2792 | 1881 | 3806 | 1846 | 3366 | 1522 | 3570 | 1212 | 7204 | 1245 | 2136 | 1484 | 2546 | 1447 | 2737 | 1667 | 2153 | 849 | 880 | 752 | 781
Measurement IOPS | 888 | 909 | 1085 | 832 | 906 | 1123 | 973 | 959 | 920 | 1070 | 1045 | 943 | 1083 | 954 | 1027 | 1130 | 1141 | 1081 | 1106 | 896 | 1028 | 1105 | 887 | 1037 | 874 | 959 | 936 | 782 | 1034 | 949 | 949 | 932 | 902 | 884 | 986 | 876
At end of subinterval 78, looking back a short distance, not enough subintervals to have “seen enough”
At this point, we “saw enough” to declare success and stop

## Slide 9: We can get good results from just IOPS, service time
With measure=on, if we set the accuracy_plus_minus and confidence parameters reasonably tight, we can detect when the subsystem has “settled down” and the workload has stabilized.
When we say the subsystem has “settled down”, what we generally mean is that Write Pending has settled down.
  Detecting stability just looking at IOPS / service time means we need to be sufficiently careful (precise) so that the instability where WP hasn’t yet stabilized is enough to prevent “matching” on the accuracy_plus_minus and confidence parameters.
Thus measure=on should work just fine for any vendor's equipment, even without a proprietary "connector" to fetch internal performance data from the storage product.

## Slide 10: Faster / more robust stability detection with command device
Ivy automatically discovers and uses a command device to the target subsystems(s), if one is found on a test host and the command device connector is available.
“measure=on” has Write Pending-based stability criteria you can use with a cmd dev.
  max_wp = "2%" - default “100%”
    A subinterval sequence will be rejected if WP is above the limit at any point in the sequence.
    Use this for read tests to ensure WP is empty during the test.
  min_wp = "68%" - default “0%”
    A subinterval sequence will be rejected if WP is below the limit at any point in the sequence.
    Use this for write tests to ensure WP is full during the test.
  max_wp_range = "3%" - default “3%”
    A subinterval sequence will be rejected if WP varies up and down by more than the specified (absolute) amount at any point in the sequence. max_wp_range="3%" matches from 0% to 3%, as well as from 67% to 70%.
    Use this in general all the time so you reject periods with major movement in Write Pending.

## Slide 11: The cooldown_by_wp setting – optimize elapsed time
Whether or not you use measure=on, cooldown_by_wp is enabled if a command device is discovered and the command device connector is available.
The default is cooldown_by_wp=on
Set cooldown_by_wp=off when it is valid to carry forward WP from one test step to the next.
  This can speed up the next test step tremendously if the next step doesn’t stabilize until WP is full, AND if both steps place the SAME things into WP. (An example follows in a later slide.)
  If you are switching, say, from testing 4 KiB blocks to testing 8 KiB blocks, then after you make two trials, one with cooldown_by_wp set to on and one set to off, you can see if carrying WP over from the previous step with the different blocksize makes a difference. After seeing and thinking about it, will know if cooldown_by_wp=off is OK.

## Slide 12: Designing your test to run in mimimal time
Use min_wp / max_wp / max_wp_range with measure=on to measure only when wp has stabilized.
  Lets you use looser accuracy / confidence parameters for a faster test if you don’t need a meticulously accurate result, without losing detection of WP stabilization.
With or without measure=on, use cooldown_by_wp where appropriate to carry WP contents forward from one test step to another, to minimize warmup time.
cooldown_by_wp=off uses a single cooldown subinterval

## Slide 13: warmup_seconds, measure_seconds, subinterval_seconds
warmup_seconds – default = 5
measure_seconds – default = 60
With measure=off, the warmup and measurement periods are fixed.
With measure=on, these values represent minimum periods during automatic detection of a valid measurement.
subinterval_seconds default is 5
  Don't make this shorter, but if you are running really long test steps, you could use longer subintervals to reduce the volume of csv output.

## Slide 14: Specifying measure=on – source=workload
source=workload is always available – the test host view of I/O timing.
  Fully explained in "programming ivy" material.
  (There is also source=RAID_subsystem, not shown here.)
I/O events are accumulated over a subinterval, and rolled up according to category
  category = overall, read, write, random, sequential, random_read, random_write, sequential_read, sequential_write
  Within these categories, there are also service time / response time histograms that are kept and shown in ivy output csv files.

## Slide 15: accumulator_type, accessor
For each I/O, the service time is posted into one "accumulator", the bytes transferred into another, and if IOPS=max is not set, we post "response time" into another.
  accumulator_type = bytes_transferred, service_time, response_time
  Service time is from I/O launch to I/O completion. Response time is from scheduled I/O start to I/O completion.
    I/Os will not launch at the scheduled time if there is no "tag" available, so response time can be longer than service time.
    IOPS=max sets every I/O's scheduled time to zero, in which case "response time" is not posted.
Retrieve data from a (rolled up) accumulator using an accessor
  accessor = avg, count, min, max, sum, variance, standardDeviation
  Use avg for service_time, response_time which are in seconds.
  Use sum for bytes_transferred. Divide by subinterval_seconds to get bytes per second.
  Divide service_time's count by subinterval_seconds to get IOPS.

## Slide 16: focus_rollup
The detection of a valid measurement is performed at the granularity of the focus_rollup.
  A measurement subinterval sequence constitutes a valid measurement if for all instances of the focus rollup the validity criteria were met.
The default is focus_rollup="all", which looks for an overall valid measurement across all workload threads across all test hosts.
If you have created a rollup by port, by saying
  [CreateRollup] "port";
  then you can specify focus_rollup="port", and then for measure=on, ivy will look for a simultaneous valid measurement period on each instance of the port rollup.

## Slide 17: An example of running a test in minimum time
Here we are doing a 4K random I/O run with IOPS=max, and we are showing the IOPS we get for 0%, 25%, 50%, 75%, and 100% writes.
We start out by doing the 0% read step, with min_wp=“68%” and cooldown_by_wp=off
  It takes some time to warm up because WP needs to fill up and stabilize.
  The measurement itself takes a little extra time as the IOPS is not quite as stable when the subsystem is in emergency destage, and the subsystem takes some time to “switch gears” and for the IOPS to become stable once WP is full.
The 25% reads, 50% reads – cooldown_by_wp=off
  The previous step leaves WP full, and we stabilize very quickly. It’s OK as what we are putting into WP (4K random writes) is the same thing that is draining out (4K random writes to the same LDEVs)
The 75% reads step – cooldown_by_wp= on
The 100% read step – could use max_wp=“2%”, but not necessary (previously cooldown_by_wp=on)

## Slide 18: Example – minimum time % read test - output
Test Name | Step Number | Step Name | Start | Warmup | Duration | Cooldown | iogenerator type | blocksize | maxTags | IOPS | fractionRead | Overall IOPS
read_vs_write | step0001 | read_0 | 4/22/2015 11:30 | 02:05.0 | 00:50.0 | 00:05.0 | random_steady | 4 KiB | 16 | max | 0 | 893.20
read_vs_write | step0002 | read_25 | 4/22/2015 11:31 | 00:10.0 | 00:55.0 | 00:05.0 | random_steady | 4 KiB | 16 | max | 0.25 | 1,128.00
read_vs_write | step0003 | read_50 | 4/22/2015 11:32 | 00:10.0 | 00:50.0 | 00:05.0 | random_steady | 4 KiB | 16 | max | 0.5 | 1,533.86
read_vs_write | step0004 | read_75 | 4/22/2015 11:33 | 00:10.0 | 00:50.0 | 06:45.0 | random_steady | 4 KiB | 16 | max | 0.75 | 2,077.54
read_vs_write | step0005 | read_100 | 4/22/2015 11:41 | 00:15.0 | 00:50.0 | 00:05.0 | random_steady | 4 KiB | 16 | max | 1 | 3,492.94
Warmup includes filling Write Pending and stabilizing after WP is full
cooldown_by_wp = off
cooldown_by_wp = on

## Slide 19: Conclusion
“Seen enough and stop” is effective to perform tests in minimum time.
  Without a command device, we need tighter accuracy/confidence settings and thus a bit longer test time.
  With a command device, we directly observe when WP stabilizes.
Standard small sample set math is effective with a 2x fudge factor.
  Distribution may not be a “normal distribution”, but using the +/- accuracy and confidence % specifications for a normal distribution (“student’s t-distribution) is effective to detect stability / establish needed length of measurement to adapt to the degree of instability in the measured results from subinterval to subinterval.
  Because there is some correlation from subinterval to subinterval, achieved plus/minus accuracy is somewhat looser than specified. Specify 2x tighter accuracy to be sure.

## Slide 20: Questions and Discussion

## Slide 21: Thank You