## Slide 1: Getting started with ivy
Allart Ian Vogelesang ian.vogelesang@hitachivantara.com
2020-02-10

## Slide 2: Audience – new ivy users
Recommended to go through the “Introduction to ivy” presentation first.
  Management view - reduced cost, improved data quality, faster time-to-market, etc.
This "getting started" presentation is intended for new ivy users.
  Explain essential concepts
  First look at ivy engine control statements
    [Hosts], [CreateWorkload], [CreateRollup], [EditRollup], [Go]
  Guided tour of some key aspects of ivyscript programs.
After reviewing this material, the new user will be better prepared to start exploring existing ivyscript programs, and to start coding ivyscript.
To learn more, see the comprehensive “ivyscript reference” and “programming the ivy engine”, and "ivy adaptive PID" presentation materials.

## Slide 3: How ivy was installed
ivy family executables were put in a folder somewhere.
This folder was put into the PATH for both foreground and background processes in Linux using a script in /etc/profile.d
  ivydriver starts on each test host via ssh as a background process where “bash profile” type scripts don’t apply.
Certificate-based ssh authentication as root was set up between the ivy central host and all test hosts.
The InquireAbout executable was marked “setuid” and owned by root in order run as root to issue SCSI Inquiry commands to raw LUNs. There is a handy script to do this.
  This lets ordinary users use showluns.sh independent of ivy.
Note: You must be root to run ivy, since it opens raw LUNs to do I/O.

## Slide 4: ivy family executables
LUN_discovery suite showluns.sh, InquireAbout, etc.
  Open source https://github.com/Hitachi-Data-Systems/LUN_discovery
  Decodes Hitachi storage SCSI Inquiry attributes, e.g. port, LDEV, LDEV_type, Pool_ID, etc.
ivy ivy, ivydriver, ivy csv utilities
  Open source https://github.com/Hitachi-Data-Systems/ivy
ivy command device connector ivy_cmdev
  Hitachi proprietary. Not open source. Restricted to authorized internal Hitachi lab use with license key.
  Other storage vendors can see the interface in ivy’s source code to ivy_cmddev, and are encouraged to develop a similar ivy configuration and real-time performance monitoring interface for their own products, and to contribute to the ivy project overall.

## Slide 5: showluns.sh
The LUN_discovery SCSI Inquiry tool suite is its own separate open source project on github, but is installed along with, and serves as a front-end to ivy. This is what makes ivy vendor-independent.
Try typing “showluns.sh”, or type "showluns.sh >x.csv" and open x.csv in Windows with Excel.
This produces a csv file with a header line with LUN SCSI Inquiry attribute names, and one data line for each /dev/sdxx LUN with the corresponding attribute values for that LUN.
  hostname,LUN_name,LDEV,port, … sun159,/dev/sdc,00:00,1A, … sun159,/dev/sdd,00:01,2A, …
The showluns.sh output csv file only shows those attribute names for which at least one LUN provided a non-empty value.
  And thus depending on what kinds of LUNs the SCSI Inquiry tool “sees”, you may get a different set of attribute names (csv columns) appearing/disappearing.
To provide support for a different vendor’s architecture and terminology in ivy, all you need is a SCSI Inquiry tool decoding that vendor's attributes providing the equivalent csv file.

## Slide 6: LUN attributes
The attributes of the LUNs that were discovered using showluns.sh become what you can select on in ivy.
For the vast majority of attribute names, the stock (vendor independent) ivy functionality is all you need to select test LUNs, e.g. [select] << { "port" : [ "1A", "2A" ] } >>
ivy also provides a couple of “specially implemented for Hitachi” attribute value matching functions to recognize shorthand for LDEV ranges and PG name ranges.
“raw strings” start with << and end with >>, making it easy to include quote marks within a string
[select] clauses are in JSON format. This is formal JSON, but ivy also supports simplified "ivy relaxed JSON"

## Slide 7: What if a Linux reboot changes /dev names?
Nothing happens.
You don’t select your test configuration by LUN name, instead, you select by LUN attribute value.
But if you really did want to select on /dev name, you can do that:
[select] << { "LUN_name" : [ "/dev/sdb", "/dev/sdc" ] } >>

## Slide 8: All discovered LUNs -> available test LUNs
Each test host, when it first wakes up, runs showluns.sh, and sends the output to the central host. The aggregated data from all test hosts forms all discovered LUNs.
All discovered LUNs includes information on all /dev/sdxx LUNs, including test host boot volumes. This goes in the output folder as all_discovered_LUNs.csv.
On the [hosts] statement, there must be a [select] clause that specifies at least one of serial_number or vendor. This is intended to prevent accidentally writing on test host boot volumes.
All discovered LUNs is filtered and LUNs matching the [hosts] statement [select] clause form “available test LUNs”. This goes in available_test_LUNs.csv.
All discovered LUNs is never used again. Later when we create workloads, this selects from available test LUNs.
showluns.sh on each test host
All discovered LUNs
Filtered by [hosts] statement [select] clause
Available test LUNs

## Slide 9: ivyscript programs start with the [hosts] statement
[Hosts] "sun159, testhost[1-8]" [Select] "serial_number : 123456, LDEV : 00:00-01:FF";
This shows ivy relaxed JSON that lets you omit outer braces {}, omit quote marks around things ivy recognizes. Ivy also supports writing this in official well-formed JSON like [Select] << { "serial_number":123456, "LDEV":"00:00-01:FF" } >>;
This selects
sun159, testhost1, testhost2, …, testhost8
The [select] query is used to filter all discovered LUNs to arrive at available test LUNs.
serial_number uses the default built-in attribute matcher
LDEV uses a special case Hitachi specific attribute matcher that recognizes LDEV ranges.

## Slide 10: [CreateWorkload]
[CreateWorkload] "fluffy" [select] << "port" : "1A" >> [iosequencer] "random_independent" [parameters] "IOPS=max, blocksize=8KiB, fractionRead=100%,maxTags=32";
We create a “flock” of workloads each with this name on a selected group of available test LUNs.
Selects from available test LUNs. [select]"" or omit [select] entirely to select all available test LUNs.
random_steady, random_independent, or sequential
Each I/O sequencer type will have its own set of parameters or settings that it uses.

## Slide 11: WorkloadID, e.g. sun159+/dev/sdc+frantic
Every workload is identified by its WorkloadID, which has three parts joined with plus signs.
ivyscript_hostname is what you called it on the [hosts] statement, which could be an alias or IPV4 dotted quad.
For training / ivy development purposes you can run a “fake” ivy multi-host configuration on one host using the IPV4 address or an alias as a second host. Each resulting instance of ivydriver is unaware of any others on the same host.
The first two parts of a WorkloadID together form the AIO context LUN ID ivyscript_hostname+/dev/sdxx
The last part of the WorkloadID is the workload name from “create workload”
by-host subthread
by host subthread
by host subthread
ivy master host
ivy main thread
[hosts] statement
testhost1
ivydriver main thread
Core 1
Workload thread
Core 2
Workload thread
LUN
Workload
Workload
Workload
testhost2
…
…
[CreateWorkload] statement
ivyscript hostname
LUN name
workload name from [CreateWorkload]
LUN's attributes come from showluns.sh
LUN
Workload
Workload
Workload
LUN
Workload
Workload
Workload
LUN
Workload
Workload
Workload
LUN
Workload
Workload
Workload

## Slide 12: What is an ivy "rollup"?
A "rollup" is a grouping of workloads.
Each workload is attached to a LUN, and this LUN has attributes like "Port", "LDEV", "LDEV type", "Pool ID", "Parity Group", "Consistency Group", "Serial Number", "Host", "Size GiB", "Vendor", "Product", "Port WWN", "CLPR", etc. These come from "showluns.sh".
A "rollup" is a way of grouping the workloads by LUN attribute.
No matter how you created the workloads, whether you selected by one of these attributes, or if you just created workloads on all available test LUNs, to get output data sliced and diced by port, say [CreateRollup] "port";
The "port" rollup has instances like "1A", "2A", etc.
Every workload (like sun159+/dev/sdc+frantic) belongs to exactly one instance in every rollup.
You can make multiple rollups on different attributes to get data sliced & diced in different ways.

## Slide 13: Rollups are key to how the ivy engine works
Rollups are used to group workloads, to navigate between (in both directions), say, a port name 1A and those workloads on LUNs mapping to port 1A.
  By-rollup csv files show data rolled up by rollup instance from results by individual WorkloadID.
  [EditRollup] uses rollups in the other direction, to send, for example, IOPS=1000 to the workloads on port 1A.
When driving multiple subsystems: [CreateRollup] "serial_number+port";
  serial_number and port must be valid LUN attribute names.
In every rollup, each WorkloadID appears in exactly one rollup instance.
  "Serial_Number+Port"
    "410123+1A"
      "sun159+/dev/sdx+workload_name", "cb28+/dev/sdy+workload_name"
Rollup type
Rollup instance.
List of WorkloadIDs comprising the rollup instance
To print this rollup structure out, say print(ivy_engine_get("rollup_structure"));

## Slide 14: You make rollups for four reasons
To get an output csv file with a csv folder by rollup type (e.g. port) and csv files by rollup instance (e.g. 1A)
  This is how you get custom "sliced & diced" data.
To perform IOPS dynamic feedback control (dfc=PID) at the granularity of the rollup instance.
  One of the demos shows measuring IOPS at MP 50% busy at the granularity of the MPU, meaning to vary the IOPS up and down separately/independently for each MPU to achieve 50% busy MP cores in that MPU.
To identify a valid measurement period at the granularity of the rollup instance using measure.
  For the valid period, when measuring at the granularity of the rollup instance, the data for each rollup instance individually met the +/- accuracy % criteria for a valid measurement. (For every port, the individual data for that port met the +/- accuracy criterion.)
To validate the test configuration as operating correctly
  E.g. Validates that the number of ports reporting was what you expected
  E.g. Validate that no one port had an IOPS too far below the highest IOPS seen on any port.

## Slide 15: Statements – [CreateRollup]
[CreateRollup] "port" [nocsv] [quantity] 64 [MaxDroop] "20%";
[nocsv] - Optional - suppresses creation of port output csv files for this rollup.
[quantity] 64 - Optional - marks the test result invalid if there aren’t 64 port instances reporting data .
[MaxDroop] "20%"
  Optional - marks the test result invalid if any one instance of the rollup has an IOPS more than 20% below that of the fastest instance.
  Useful to catch the situation where, say, one port is running slowly compared to the others because it’s in error recovery.

## Slide 16: The "all" rollup
There is always a special "all" rollup which only has one instance "all".
The "all=all" instance contains all workloads.
The "all" rollup is automatically created, and you cannot delete it.
For example [EditRollup] "all=all" [parameters] "IOPS=max"; will set IOPS=max in every workload.
Every rollup has its summary csv file folder in the [OutputFolderRoot] directory.
  Look at the "xxx.all.summary.csv" file in the "all" subfolder of the ivy output folder to get the overall summary data.

## Slide 17: [EditRollup]
The rollup concept gives you great flexibility to send out parameter setting edits to selected workloads.
First create a rollup, e.g. [CreateRollup] "LDEV_type";
Then you can say, for example
  [EditRollup] "LDEV_type=DP_vol" [parameters] "IOPS=1000";
To send a parameter change globally, say
  [EditRollup] "all=all" [parameters] "IOPS=1000";
The underlying ivy engine C++ API edit rollup call is what’s also used internally within the ivy engine to send out Dynamic Feedback Control IOPS edits in real time at the granularity of the rollup instance while the workloads are running and driving I/O.

## Slide 18: An ivy test step – a series of subintervals
There may be zero or more warmup subintervals (warmup_seconds), at least one measurement subinterval (measure_seconds), and zero or more cooldown subintervals (cooldown_seconds).
Without the measure feature, warmup and measurement run for a fixed number of subintervals.
When using the measure feature, e.g. measure = service_time_seconds with accuracy_plus_minus = 1%, warmup_seconds and measure_seconds become minimums which will be extended as long as necessary (up to timeout_seconds) to reach the +/- target accuracy.
Either way, if a command device connector is available, cooldown may be extended at zero IOPS using cooldown_by_WP and cooldown_by_MP_busy, which both default to on.
Subinterval 0
Subinterval 1
Subinterval 2
Subinterval 3
Subinterval 4
warmup
measurement
cooldown
First measurement subinterval
Last measurement subinterval

## Slide 19: The default [Go] statement
[Go];
    Default subinterval_seconds = 5
    Default warmup_seconds = 5
    Default measure_seconds = 60
    Default cooldown_seconds = 0
    Default cooldown_by_wp = "on"
      If you have a command device and the proprietary command device connector software, and a license key for the subsystem serial number, more cooldown subintervals at IOPS=0 (zero) continue until Write Pending in all CLPRs being used is empty.
  Useful when you are developing an ivyscript workflow and you just want to see quick sample csv files.
These parameters support notation like 1:00:00 (one hour), or 30:00 (30 minutes).

## Slide 20: The ivy engine and ivyscript
The ivy engine is written in C++ and can be operated directly via the ivy engine C++ API.
The ivy engine REST API and the ivyscript interpreter both let you “create workload”, “create rollup”, "go", etc.
In ivyscript, when you see a statement starting with a word in square brackets like [Hosts], [CreateWorkload], etc. this reflects an access to the corresponding underlying ivy engine C++ API call that you are making to operate the ivy engine, and the remainder of the statement shows which operands are being provided, e.g. [parameters].
  [CreateWorkload] and [ create workload ] are equivalent.
Every time you run an ivyscript program, you get a log file of all the underlying ivy engine C++ API calls that were performed in the course of running the ivyscript program.
by-host subthread
ivy master host
ivy
…
testhost1
Core 1
Workload thread
LUN
Workload
Workload
Workload
ivydriver
ivy engine C++ API
ivy engine REST API
ivy executable using the ivyscript interpreter
See “Programming the ivy engine.pptx”
See “ivyscript reference.pptx”

## Slide 21: ivyscript
Ivyscript is a bare-bones (very basic) scripting language that looks like C/C++.
Three types: string, int, and double.
The usual if statements, for loops, nested code blocks, user defined functions, etc.
Special statements starting with square-brackets tokens like [hosts] are where ivyscript exposes the underlying ivy engine C++ API call.
ivyscript and the ivy engine C++ API now have ivy_engine_get() and ivy_engine_set() functions, but many older individual ivyscript ivy engine built-in accessor functions to get things from the ivy engine still work and now map onto the appropriate ivy engine C++ API ivy_engine_get() call.
  E.g. ivy_engine_get("summary_csv")retrieves the filename of the summary csv file.
(floating point)

## Slide 22: Our first “config discovery” ivyscript program
This starts ivydriver on all the test hosts, and selects available test LUNs, and it makes csv files of all discovered LUNs and available test LUNs.
With a command device, you get subsystem configuration csv files, and the description of LUNs in available test LUNs will be augmented with config info from the subsystem.
It’s an easy way to confirm your test setup.
ivyscript string expression for set of test hosts. Here we are giving the ivy engine a string constant.
An ivyscript program is a series of statements, and each statement ends with a semicolon ;
string expression for select clause to pick available test LUNs.
[hosts] "table, chair[1-6]" [select] "serial_number : 123456";

## Slide 23: Looping over workload parameter settings
[hosts] "table, chair[1-6]" [select] "serial_number : 123456";
[CreateWorkload] "steady" [select] "" [iosequencer] "random_steady" [parameters] "IOPS=max, fractionread=100%, maxTags=32";
[Go!] << blocksize = (4KiB, 8192, 16KiB, 32KiB, "64 KiB"), measure_seconds = 30 >>;
Example of embedded quotes inside a raw string.
Create a flock of workloads each named “steady”
This null select creates a workload on all available test LUNs.
random_steady, random_independent, or sequential
"raw strings" are character strings starting with << and ending with >>, which makes it easy to have embedded quotes .
If there is no space between "4" and "KiB", then putting quotes around 4KiB is optional.
100% and 1.0 mean the same thing and are interchangeable in ivy.

## Slide 24: Same thing but looping in ivyscript
[hosts] "table, chair[1-6]" [select] "serial_number : 123456"; [CreateWorkload] "steady" [select] "" [iosequencer] "random_steady" [parameters] "IOPS=max, fractionread=100%, maxTags=32"; int blocksizeKiB; for blocksizeKiB = { 4, 8, 16, 32, 64 } { [EditRollup] "all=all" [parameters] "blocksize = \"" + string(blocksizeKiB) + "KiB\"" ; [Go!] "stepname=\"" + string(blocksizeKiB) + " KiB\", measure_seconds = 30"; };
The stepname shows up in the output csv files to auto-populate the legend for a data series.
Makes it easy to make Excel charts.
Create a flock of workloads each named “steady”
This null select creates a workload on all available test LUNs.
random_steady, random_independent, or sequential
Traditional C-style for loops are also supported
“all=all” selects all workloads
Building a string that looks like “blocksize = 4 KiB”
[EditRollup] sends a parameter update to selected workloads.

## Slide 25: [CreateRollup] examples
[hosts] "table, chair[1-6]" [select] "serial_number : 123456"; [CreateWorkload] "steady" [select] "" [iosequencer] "random_steady" [parameters] "IOPS=100, fractionread=100%, maxTags=32"; [CreateRollup] "Port"; [CreateRollup] "Serial_Number+Port"; [CreateRollup] "MPU"; // only with a command device [CreateRollup] "host+LUN_name+workload"; // same as workloadID [CreateRollup] "workloadID"; print("Rollup structure:\n" + ivy_engine_get("rollup_structure") + "\n"); [Go] "stepname=step_eh, warmup_seconds = 5, measure_seconds = 5";

## Slide 26: Retrieve result of a test step, to decide what to do next
Assume we would like to retrieve the overall IOPS value from test step 0, in order to decide what to do in step 1.
string summary_filename = ivy_engine_get("summary_csv"); double step0_IOPS = double(csv_cell_value(summary_filename,0,"Overall IOPS")); string s = "step 0 result – overall IOPS = " + string(step0_IOPS) + "\n"; print (s); log(masterlogfile(),s);
ivy csv utilities let you access a csv file like a spreadsheet.
  ivy test steps ([Go] statements) are numbered from zero, and within a test step, subintervals are numbered from zero.
  ivy csv utilities number the csv header line as line number -1 (minus one). This means the row number is the test step number in summary csv files, and the row number is the subinterval number for by-subinterval test step detail csv files.
  You typically refer to columns by the text used in the header line with column title text, but you can also retrieve by column number.
Always works to use ivy engine accessor built-in functions to generate summary csv file name.
ivy csv utility returning string value of what was between the commas in the requested row and column of the csv file.

## Slide 27: End of guided tour.
Enjoy discovering the new things you can do in ivy.