## Slide 1: Introduction to "ivy"
Block storage synthetic workload generator with real time dynamic feedback control and workflow engine. https://github.com/Hitachi-Data-Systems/ivy
Hitachi Data Systems - 2016-08-13
Allart Ian Vogelesang ian.vogelesang@hds.com

## Slide 2: Why ivy?
To automate an entire test suite workflow, performing tests in the theoretically minimum time possible
  To reduce cost
  To speed time-to-market
  To improve quality
  To automatically calibrate sales sizing tools
To simplify manual test setup
  Just say you want to test selecting pool_ID = { 0, 2 }, and let ivy figure out which LUNs on which hosts.
  Easily verify actual test configuration – say [CreateRollup] "port" [quantity] 64 [MaxDroop] 20%; and ivy will automatically validate that there are 64 ports reporting and that none of them is reporting an IOPS more than 20% below the IOPS of the fastest port.
To offer Dynamic Feedback Control measurements like "find the IOPS to obtain 1.0 ms service time"
To secure customer trust in measurement results made using open source software

## Slide 3: What does it mean – a “valid” measurement
Valid results are repeatable
  If you run the test again, within the specified +/- experimental error, you will get the same result again.
  Valid, repeatable, results are for steady-state conditions
If the workload / subsystem are not steady-state, you can’t make a valid measurement.
  After imposing a workload on the subsystem
    we need to wait for the behaviour to settle down into a steady state, waiting for initial transient conditions to settle down, then
    depending on how much "noise" there is in what is being measured, measure for long enough to obtain a valid measurement to a specified plus/minus accuracy.

## Slide 4: Scalable: master host => test host => LUN => workload
In ivy, you can layer multiple named “workload” I/O generator threads on LUNs on test hosts.
Each workload thread uses an I/O sequencer plug-in that generates I/Os in scheduled I/O start time sequence.
  We try to keep a few I/Os “pre-computed” and ready to go at all times.
  Generalized interface allows use of any I/O pattern generator, e.g. synthetic or in future, playback.
Use of C++ with Linux kernel Asynchronous I/O interface means each workload thread can drive any queue depth up to limits of the OS / HBA with state of the art minimal CPU overhead.
testhost1
OS
LUN
HBA
LUN
LUN
HBA
LUN
Ivyslave main thread
Workload
Workload
Workload
Workload
Workload
Workload
Workload
Workload
Workload
NIC
Workload
Workload
Workload
by-host subthread
NIC
testhost2
OS
LUN
HBA
Workload
Workload
Workload
by host subthread
by host subthread
ivy master host
Ivy main thread
[hosts] statement
[CreateWorkload] statement

## Slide 5: An ivy test is a sequence of "subintervals"
[optional] gather from command device
Subinterval n-1
Subinterval n
Subinterval n+1
Subinterval n+2
typically 5 seconds
Roll up host workload data
The default is subinterval_seconds = 5
If a command device connector is being used, the performance data for the subinterval arrive at ivymaster and are posted using configuration filters by rollup instance.
At end of subinterval, workload thread measurement data are sent to ivymaster to be rolled up.
If dynamic feedback control (dfc=PID) is being used, DFC parameter updates at the granularity of the rollup instance are sent out
ivymaster decides to continue the test for another subinterval, or to stop.
continue
continue
continue
[optional] send out iogenerator parameter changes (dynamic feedback control)

## Slide 6: A "successful" test step (subinterval sequence) – 3 phases
During the warmup phase, we are either allowing time for, or expressly waiting for, initial transient conditions to settle down.
  warmup_seconds specifies the minimum warmup period, which the measure feature may extend
When the test step is declared a "success", the results of the test step are defined as the average/totals over the measurement phase.
  measurement_seconds specifies the minimum measurement period, which the measure feature may extend
  A test step may be declared a "failure" by the measure feature upon reaching the timeout_seconds value without observing a valid measurement. In this case, all subintervals are posted as "warmup" subintervals.
During the cooldown phase, we are running at least one extra subinterval continuing to drive the workload, so that even with some time jitter across test hosts, the full workload will have been running throughout the measurement.
  If a "command device connector" is being used, cooldown_by_wp=on controls whether to subsequently keep running even more subintervals with IOPS=0 until we see that Write Pending in the subsystem has emptied.
Subinterval 0
Subinterval 1
Subinterval 2
Subinterval 3
Subinterval 4
Subinterval 5
Subinterval 6
Subinterval 7
warmup
measurement
cooldown

## Slide 7: measure parameters
accuracy_plus_minus = 5%
  Default is 5%.
  Extend the warmup as necessary until initial transients die down and extend the measurement period as necessary until we have "seen enough" to be sufficiently confident we have made a measurement to the specified accuracy.
confidence = 95%
  How confident you need to be that your measurement falls within the specified plus or minus range around the long term average that you would get measuring forever.
  Default is 95%, meaning measurement falls within accuracy_plus_minus 19 times out of 20.
  Ivy has a menu of 11 specific pre-loaded confidence values that you pick from.
    50%, 60%, 70%, 80%, 90%, 95%, 98%, 99%, 99.5%, 99.8%, and 99.9%

## Slide 8: Standard statistical formulas are used
It is both convenient and effective to use the standard statistical formulas using the accuracy_plus_minus and confidence parameters
  http://en.wikipedia.org/wiki/Student%27s_t-distribution (for the math literate)
Limitation – the standard formulas don't exactly apply to ivy
  The formulas are for samples drawn at random from a large population.
  The behaviour / measurement for one subinterval is related to those for preceding / succeeding subintervals, thus "gaming the system".
Rule of thumb to correct for this
  Specify accuracy_plus_minus with a 2x safety factor, and you'll be OK.
    Say accuracy_plus_minus = 5% to get repeatability within 10%.

## Slide 9: measure parameter "shorthand" presets
measure = IOPS measure = MB_per_second measure = service_time_seconds measure = response_time_seconds
These are "shorthand" for a particular combination of more detailed parameter settings
  See "ivy programmer's reference, part two" for a description of the full set of parameter settings.

## Slide 10: measure=IOPS, accuracy_plus_minus=5%
Chart: Subinterval number
 | 1007.8948 | 996.8373 | 1004.7242 | 975.4997 | 1000.5075 | 1011.4983 | 1003.8226 | 1024.5235 | 993.0908 | 984.1016 | 976.8074 | 1005.2629 | 976.8081 | 1015.6425 | 1017.5525 | 1017.4326 | 1010.8694
 | 668.6441 | 568.1569 | 1272.9616 | 1228.5412 | 1101.8844 | 646.2105 | 1040.4471 | 1373.2667 | 991.6476 | 1322.3557 | 784.1122 | 686.6811 | 996.562 | 1302.7766 | 924.5647 | 940.0251 | 1409.4197
Both curves long term average is 1000.0 IOPS

## Slide 11: measure=IOPS, accuracy_plus_minus=5%
The ivy "measure" feature extends the test until enough measurements have been made to be sufficiently statistically confident that the average of the by-subinterval values is within a specified accuracy_plus_minus variation from what the long term average would be continuing to test indefinitely.
Chart: Subinterval number
 | 1007.8948 | 996.8373 | 1004.7242 | 975.4997 | 1000.5075 | 1011.4983 | 1003.8226 | 1024.5235 | 993.0908 | 984.1016 | 976.8074 | 1005.2629 | 976.8081 | 1015.6425 | 1017.5525 | 1017.4326 | 1010.8694
 | 668.6441 | 568.1569 | 1272.9616 | 1228.5412 | 1101.8844 | 646.2105 | 1040.4471 | 1373.2667 | 991.6476 | 1322.3557 | 784.1122 | 686.6811 | 996.562 | 1302.7766 | 924.5647 | 940.0251 | 1409.4197
Both curves long term average is 1000.0 IOPS

## Slide 12: measure effective to automatically reject initial transients
Chart: Seconds
Warmup IOPS | 34402 | 42682 | 46147 | 46135 | 46197 | 47208 | 9018 | 1836 | 802 | 8209 | 7929 | 213 | 10891 | 7723 | 2722 | 3181 | 3093 | 3856 | 2838 | 2084 | 2792 | 1881 | 3806 | 1846 | 3366 | 1522 | 3570 | 1212 | 7204 | 1245 | 2136 | 1484 | 2546 | 1447 | 2737 | 1667 | 2153 | 849 | 880 | 752 | 781
Measurement IOPS | 888 | 909 | 1085 | 832 | 906 | 1123 | 973 | 959 | 920 | 1070 | 1045 | 943 | 1083 | 954 | 1027 | 1130 | 1141 | 1081 | 1106 | 896 | 1028 | 1105 | 887 | 1037 | 874 | 959 | 936 | 782 | 1034 | 949 | 949 | 932 | 902 | 884 | 986 | 876
At end of subinterval 78, looking back a short distance, not enough subintervals to have “seen enough”
At this point, we “saw enough” to declare success and stop
WP
IOPS

## Slide 13: Initial study - 60% test time reduction, better quality
Instead of running for a fixed 6 minutes for each step of the several hundred combinations / permutations of a standard scalability test sequence, when a variable step run time using measure was used
  Overall test run time decreased by 60%
    The vast majority of the time workloads settled down quickly and were then stable.
  Quality was improved
    In some rare cases, there were test steps that needed to run for 20 minutes to get an accurate measurement.
The use of the measure feature in ivy substantially reduces test time, while at the same time improving quality.

## Slide 14: ivy – achieving vendor independence
An external vendor proprietary simple SCSI Inquiry-based LUN discovery tool is used.
  The external tool provides a "discovered LUNs" csv file that has a header line with column titles
    host,LUN name,HDS product,port,LDEV,PG,CLPR, … testy1,/dev/sdxy,VSP,1A,00:00,1-1,CLPR0, … testy1,/dev/sdyz,VSP,2A,00:01,1-2,CLPR0, …
  To support another vendor's architecture or terminology, all you need is the external LUN discovery tool that produces such a csv file.
  Hitachi LUN discovery tool is open source - https://github.com/Hitachi-Data-Systems/LUN_discovery
In ivy, the LUN discovery csv file header line column titles become selectable
  [select] "port" is { "1A", "3A", "5A", "7A"}, "CLPR" is "CLPR0"

## Slide 15: "command device connector" is proprietary extension to ivy
Available only for authorized use in Hitachi labs, with license key mechanism.
Transparently / automatically connects to a command device if one is available.
Retrieves subsystem configuration data
  Enables selection of test configuration by subsystem configuration attributes such as drive_type.
Retrieves real time subsystem performance data, aligned with test subintervals.
  Records what is happening inside the subsystem correlated with what the hosts are seeing.
  Enables real-time dynamic feedback control of host workload based on subsystem data
  "measure IOPS at 50% owning MP core % busy", or "measure IOPS at 50% parity group percent busy"
Checks that subsystem does not have any failed components.

## Slide 16: Other vendors – make your own connector
Vendors are encouraged to prepare their own proprietary "subsystem connector" interface tools to be used with ivy.
  Collect subsystem configuration data to augment SCSI Inquiry attribute data
  Collect real time subsystem performance data, synchronized and aligned with test host workload data.
    Facilitates development of modeling tools.
  Use dynamic feedback control to find the IOPS to reach a target value for
    subsystem MP % busy, or
    drive % busy, or
    cache dirty data % full, etc.
Output from demo runs includes examples of output using a Hitachi command device connector.
This is to show you that with ivy, you too can do dynamic feedback control on your own real-time metrics if you write your own ivy connector.

## Slide 17: [CreateRollup] "port";
Every workload thread is represented in exactly one instance of each rollup.
There is by default always a rollup called "all" which has one rollup instance, "all=all" which consists of all workloads on all LUNs on all hosts.
A user-defined rollup name must be combination of LUN attribute names.
  If you have multiple subsystems under test, to get data by subsystem by port say [CreateRollup] "serial_number+port"; and get instances like "serial_number+port=410034+1A".

## Slide 18: "Everything" in ivy works using rollups
You get csv files by rollup instance
  Say [nocsv] to suppress.
Both the "measure" functionality, and the dynamic feedback control functionality (dfc=PID) operate at the granularity of the rollup instance (fine grained)
  To do this on subsystem data, with a command device connector, a "configuration filter" is built in advance for each rollup instance showing which underlying hardware instances to filter on for that rollup instance, e.g. port={1A, 3A}, MPU=03, … This includes indirectly associated hardware inferred by examining subsystem configuration data.
[CreateRollup] "port" [quantity] 64;
  Will invalidate a measurement if we don't get data for exactly 64 subsystem ports.
[CreateRollup] "port" [MaxDroop] 20%;
  Invalidates if there is a port whose IOPS is more than 20% slower than the fastest port.
Are all 64 cables working?
Any ports running slow?

## Slide 19: industry standard "PID Loop" controller
Chart: Subinterval number
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.250_x_baseline
1.250_x_baseline
Target service time
ivyscript automated workflow:
Not shown
  Measure max IOPS
  Measure "baseline" service time at 1% of max IOPS
Use PID loop dynamic feedback control to measure IOPS for various multiples of baseline service time

## Slide 20: Workflow plots auto-scaling IOPS vs. service time curve
Chart: IOPS
| 39.945800000000006 | 1501.84 | 1917.41 | 2417.1999999999998 | 2730.61 | 2965.8900000000012 | 3277.04 | 3321.94 | 3355.4900000000002 | 3376.55
 | 6.5622 | 6.9609 | 7.8127 | 9.49 | 11.1534 | 12.8037 | 16.1068 | 19.3879 | 25.9613 | 32.5304
ivyscript automated workflow:
Measure max IOPS
Measure "baseline" service time at 1% of max IOPS
Use PID loop dynamic feedback control to measure IOPS for various multiples of baseline service time

## Slide 21: DFC effective on command device connector data
Chart: For parity group busy % = 10%, 20%, 30%, …
| 9.950800000000011E-2 | 0.19962099999999997 | 0.29997200000000035 | 0.40008000000000027 | 0.50149100000000002 | 0.60100600000000004 | 0.70207500000000045 | 0.80312099999999997 | 0.90364599999999995 | 0.95612600000000003 | 0.99374700000000005
 | 3612.13 | 7680.14 | 11794.7 | 17398.6 | 23119.2 | 30544.7 | 39590.5 | 52291.5 | 74647.2 | 98869.1 | 153015
Actually achieved PG busy %

## Slide 22: Fine-grained dynamic feedback control
Chart: 
| 10% busy | 20% busy | 30% busy | 40% busy
MPU0 | 12574.6 | 26557.2 | 42388.2 | 57959.5
MPU1 | 9852.86 | 20783.7 | 33109.1 | 45796.2
MPU2 | 11482.2 | 25159 | 40517.9 | 55810.4
MPU3 | 9474.12 | 20309.9 | 32416.3 | 44996.2
IOPS

## Slide 23: Service time histograms
Chart: Read Service Time at 90% of max IOPS
| 0.0x | 0.1x | 0.2x | 0.3x | 0.4x | 0.5x | 0.6x | 0.7x | 0.8x | 0.9x | 1.x | 2.x | 3.x | 4.x | 5.x | 6.x | 7.x | 8.x | 9.x | 10.x | 11.x | 12.x | 13.x | 14.x | 15.x | 16.x | 17.x | 18.x | 19.x | 2x. | 3x. | 4x. | 5x. | 6x. | 7x. | 8x. | 9x. | 1xx. | 2xx. | 3xx. | 4xx. | 5xx. | 6xx. | 7xx. | 8xx. | 9xx. | 1xxx. | 2xxx. | 3xxx. | 4xxx. | 5xxx. | 6xxx. | 7xxx. | 8xxx. | 9xxx. | 10000+
90% of max IOPS 100% read | 0.33 | 0.073333 | 0.0066667 | 0.0033333 | 0.0066667 | 1.07 | 11.8433 | 42.4867 | 85.5067 | 120.58 | 134.537 | 129.66 | 112.63 | 98.2333 | 87.17 | 73.7767 | 63.5733 | 55.0167 | 49.4233 | 43.66 | 38.8767 | 33.6067 | 31.0333 | 28.2633 | 169.49 | 70.3267 | 31.1833 | 14.57 | 7.3933 | 3.9867 | 1.9867 | 1.1033 | 1.4033 | 0.0066667
90% of max IOPS 75% read | 0.17209 | 0.054016 | 0.012048 | 0.0072289 | 0.0086345 | 0.0040161 | 0.0040161 | 0.0050201 | 0.0032129 | 0.38133 | 4.458 | 16.9014 | 34.7841 | 50.401 | 59.4129 | 61.2412 | 58.6414 | 55.2402 | 52.0253 | 48.0966 | 43.1629 | 38.3028 | 34.3253 | 30.3819 | 26.7347 | 23.8488 | 21.912 | 20.0799 | 133.534 | 69.7528 | 41.6735 | 27.49 | 18.756 | 13.254 | 9.4034 | 6.7781 | 17.851 | 1.206 | 0.11165 | 0.01245 | 0.0012048 | 0.0002008
90% of max IOPS 50% read | 0.14984 | 0.041042 | 0.0013029 | 0.0019544 | 0.0013029 | 0.00065147 | 0.25668 | 3.3974 | 12.0319 | 22.2313 | 30.1824 | 33.0762 | 31.5713 | 28.9596 | 27.1954 | 25.542 | 23.0873 | 20.6756 | 18.4365 | 16.7016 | 15.058 | 13.7687 | 12.7752 | 12.0072 | 11.1062 | 83.6156 | 49.8358 | 32.3433 | 22.129 | 15.5837 | 11.2899 | 8.1062 | 5.8234 | 15.602 | 1.0143 | 0.10749 | 0.011075 | 0.0019544 | 0.00065147
90% of max IOPS 25% read | 0.063535 | 0.029978 | 0.00022371 | 0.00022371 | 0.00022371 | 0.11723 | 1.6479 | 5.5586 | 10.1076 | 13.4311 | 14.6676 | 13.8065 | 12.4065 | 11.3633 | 10.3899 | 9.2723 | 8.1962 | 7.3461 | 6.7763 | 6.2924 | 5.9931 | 5.6796 | 5.4711 | 5.2074 | 41.3841 | 24.8418 | 14.9168 | 9.8926 | 6.8058 | 4.9157 | 3.5902 | 2.7982 | 9.317 | 1.0611 | 0.17673 | 0.029083 | 0.0071588 | 0.0011186 | 0.00044743 | 0.00022371
90% of max IOPS 0% read
Chart: Write Service Time at 90% of max IOPS
| 0.0x | 0.1x | 0.2x | 0.3x | 0.4x | 0.5x | 0.6x | 0.7x | 0.8x | 0.9x | 1.x | 2.x | 3.x | 4.x | 5.x | 6.x | 7.x | 8.x | 9.x | 10.x | 11.x | 12.x | 13.x | 14.x | 15.x | 16.x | 17.x | 18.x | 19.x | 2x. | 3x. | 4x. | 5x. | 6x. | 7x. | 8x. | 9x. | 1xx. | 2xx. | 3xx. | 4xx. | 5xx. | 6xx. | 7xx. | 8xx. | 9xx. | 1xxx. | 2xxx. | 3xxx. | 4xxx. | 5xxx. | 6xxx. | 7xxx. | 8xxx. | 9xxx. | 10000+
90% of max IOPS 100% read
90% of max IOPS 75% read | 47.4494 | 179.16 | 11.5934 | 9.2586 | 7.1843 | 5.0932 | 4.5394 | 4.3038 | 4.1203 | 33.9386 | 19.9825 | 8.7104 | 3.2034 | 0.89197 | 0.31245 | 0.11526 | 0.047189 | 0.016667 | 0.0054217 | 0.0034136 | 0.001004 | 0.0002008 | 0.0002008
90% of max IOPS 50% read | 101.851 | 476.814 | 12.8345 | 2.3127 | 1.63 | 1.1107 | 0.85994 | 0.62997 | 0.47622 | 3.2072 | 0.9114 | 0.36482 | 0.19935 | 0.087296 | 0.057329 | 0.033225 | 0.014332 | 0.009772 | 0.0065147 | 0.0052117 | 0.0045603 | 0.0026059 | 0.0026059 | 0.0013029 | 0.00065147 | 0.00065147 | 0.0032573 | 0.0032573 | 0.0039088
90% of max IOPS 25% read | 112.717 | 674.049 | 16.9043 | 2.7485 | 1.7251 | 1.2944 | 1.0412 | 0.75839 | 0.62595 | 3.7626 | 1.2631 | 0.83535 | 0.62327 | 0.46197 | 0.3519 | 0.28971 | 0.21342 | 0.16644 | 0.13356 | 0.10447 | 0.083893 | 0.070694 | 0.05906 | 0.043624 | 0.035794 | 0.030649 | 0.025503 | 0.02528 | 0.11767 | 0.040268 | 0.0217 | 0.014541 | 0.012528 | 0.00783 | 0.006264 | 0.0049217 | 0.028412 | 0.0051454
90% of max IOPS 0% read | 788.3 | 217.327 | 6.7667 | 2.2833 | 1.3567 | 1.0033 | 0.81667 | 0.65333 | 0.62667 | 2.84 | 0.20333 | 0.01
Measuring the write service time at IOPS=max is meaningless

## Slide 24: Layered workloads can be placed within the LUN
Chart: Sequential MB/s by zone

## Slide 25: ivy in one chart
Written in C++ using Linux native kernel Asynchronous I/O interface
  Lowest CPU overhead – minimizes test host hardware cost & maximizes measurement accuracy
Designed for open source / vendor independence.
Super easy test setup – select by LDEV, by Port, by PG, Pool ID
Tests for minimum time to make a valid measurement to specified +/- % accuracy
Real-time dynamic feedback control (DFC) of workload
  "find what IOPS is needed to obtain 1.0 ms service time"
Records only valid measurement data
  Can check number of resources reporting (ports, PGs, …) and that none running too slowly.
Workflow automation using ivyscript programming language wrapper around ivy engine.

## Slide 26: Ivy development status
August, 2016
  Internal HDS performance team user beta test in progress, including test of dedupe & compression support
  Released as open source.
  Demos available for all functionality.
  Support for HUS VM, VSP Gx00.
  Support for HUS100 series.

## Slide 27: Ivy futures
Some ideas:
  Repackage access to ivy engine via a RESTful API.
    Build CLI on RESTful API to enable programming ivy in Python or any other language
    Remove outer ivyscript programming layer wrapper, exposing ivy engine control statements as CLI commands.
  Develop VSP G1000 support
  Extend VSP Gx00 support
  Develop "auto gain control" feature for PID loop
  Transition to POSIX asynchronous I/O and port to other OS platforms.

## Slide 28: Thank You