## Slide 1: Introduction to "ivy"
Block storage synthetic workload generator with real time dynamic feedback control https://github.com/Hitachi-Data-Systems/ivy
Hitachi Data Systems - 2016-08-11
Allart Ian Vogelesang ian.vogelesang@hds.com

## Slide 2: Why ivy? To automate performance testing
Reduce cost
Speed time to market
Improve quality
Simplify test setup
Measure IOPS at a specified response time (dynamic feedback control)
Get trust in measurement results through open source

## Slide 3: Scalable block storage synthetic workload generator with real time dynamic feedback control
In ivy, you can layer multiple named “workload” I/O generator threads on LUNs
Each workload thread uses an I/O sequencer plug-in that generates I/Os in scheduled I/O start time sequence.
  We try to keep a few I/Os “pre-computed” and ready to go at all times.
  Generalized interface allows use of any I/O pattern generator, e.g. synthetic or playback.
Use of C++ with Linux kernel Asynchronous I/O interface means each workload thread can drive any queue depth up to limits of the OS / HBA with state of the art minimal CPU overhead.
testhost1
OS
LUN
HBA
LUN
LUN
HBA
LUN
Ivyslave main thread
Workload
Workload
Workload
Workload
Workload
Workload
Workload
Workload
Workload
NIC
Workload
Workload
Workload
by-host subthread
NIC
testhost2
OS
LUN
HBA
Workload
Workload
Workload
by host subthread
by host subthread
ivy master host
Ivy main thread
[hosts] statement
[CreateWorkload] statement

## Slide 4: ivy in one chart
Written in C++ using Linux native kernel Asynchronous I/O interface
  Lowest CPU overhead – minimizes test host hardware cost & maximizes measurement accuracy
  Designed for open source / vendor independence.
Super easy test setup – select by LDEV, by Port, by PG, Pool ID
Can test for minimum time necessary to make a valid measurement to a specified +/- percent accuracy
Real-time dynamic feedback control (DFC) of workload
  "measure IOPS at 1 ms service time"
Records only valid measurement data
  Can check number of resources reporting (ports, PGs, LDEVs, etc.) and that none running too slowly.
Workflow automation using ivyscript programming language wrapper around ivy engine.

## Slide 5: ivy – achieving vendor independence
An external vendor proprietary simple SCSI Inquiry-based LUN discovery tool is used.
  The external tool provides a "discovered LUNs" csv file with a header line
    host,LUN name,HDS product,port,LDEV,PG,CLPR, … testy1,/dev/sdxy,VSP,1A,00:00,1-1,CLPR0, … testy1,/dev/sdyz,VSP,2A,00:01,1-2,CLPR0, …
  To support another vendor's architecture or terminology, all you need is the external LUN discovery tool that produces such a csv file.
  Hitachi LUN discovery tool is open source - https://github.com/Hitachi-Data-Systems/LUN_discovery
In ivy, the LUN discovery csv file header line column titles become selectable
  [select] "port" is { "1A", "3A", "5A", "7A"}, "CLPR" is "CLPR0"

## Slide 6: Proprietary extension – not open source
The "command device connector", or ivy_cmddev executable.
  Available only for authorized use in Hitachi labs, with license key mechanism.
  Transparently / automatically connects to a command device if one is available.
Retrieves subsystem configuration data
  Enables selection of test configuration by subsystem configuration attributes such as drive_type.
Retrieves real time subsystem performance data, aligned with test subintervals.
  Records what is happening inside the subsystem correlated with what the hosts are seeing.
  Enables real-time dynamic feedback control of host workload based on subsystem data
  "measure IOPS at 50% owning MP core % busy", or "measure IOPS at 50% parity group percent busy"
Checks that subsystem does not have any failed components.

## Slide 7: Other vendors – make your own connector
Vendors are encouraged to prepare their own proprietary "subsystem connector" interface tools to be used with ivy.
  Collect subsystem configuration data to augment SCSI Inquiry attribute data
    Select a test configuration based on subsystem configuration attributes.
  Collect real time subsystem performance data, synchronized and aligned with test host workload data.
    Facilitates development of modeling tools.
  Use dynamic feedback control to find the IOPS to reach a target value for
    subsystem MP % busy, or
    drive % busy, or
    cache dirty data % full, etc.

## Slide 8: Demos show command device connector functionality
Why, when only authorized Hitachi lab users have access?
Ivy presentation material and sample demo output & videos describe Hitachi command device connector functionality so as to
  Show what ivy was designed to do
  Serve to illustrate the functionality that other vendors could achieve by developing their own connectors.

## Slide 9: [CreateRollup] "LDEV";
A rollup is what mathematicians call a "partition" – a way to divide a collection of things (in this case host-LUN-workload threads) into subgroups.
There is by default always a rollup called "all" which has one rollup instance, also called "all" which consists of all workloads on all LUNs on all hosts.
Otherwise, a rollup name must be combination of LUN attribute names
If you have multiple subsystems under test, to get data rolled up by subsystem by port say [CreateRollup] "serial_number+port"; and get instances like "410034+1A".

## Slide 10: Rollups are multi-purpose
The default is to print csv files by rollup instance.
  Say [nocsv] to suppress.
On the [Go] statement to run a subinterval sequence, focus_rollup="PG"
  Both dfc=pid, the dynamic feedback control feature, as well as measure, the "seen enough and stop" feature operate at the granularity of the rollup instance.
[CreateRollup] "port" [quantity] 32;
  Will invalidate measurements if we don't get data for exactly 32 subsystem ports.
[CreateRollup] "port" [MaxDroop] "20%";
  Invalidates if there is a port whose IOPS is more than 20% slower than the fastest port.

## Slide 11: ivy dynamic feedback control (DFC)
Subinterval n-1
Subinterval n
Collect & rollup test host workload data (fraction of a second)
Subinterval n+1
Subinterval n+2
With DFC=PID, workload parameter updates (usually "IOPS=xxx") sent out and applied in real time to workload I/O sequencer. Does not affect I/Os in "precompute Q, ready to launch".
cmd dev subinterval may not exactly align, but offset is minimal
cmd dev gather timed so data arrive centrally just in time at end of subinterval
typically 5 seconds

## Slide 12: industry standard "PID Loop" controller
Chart: Subinterval number
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.125_x_baseline
1.250_x_baseline
1.250_x_baseline
Target service time
ivyscript automated workflow:
Measure max IOPS
Measure "baseline" service time at 1% of max IOPS
Use PID loop dynamic feedback control to measure IOPS for various multiples of baseline service time

## Slide 13: DFC on host workload data – non proprietary
Chart: IOPS
| 39.945800000000006 | 1501.84 | 1917.41 | 2417.1999999999998 | 2730.61 | 2965.8900000000012 | 3277.04 | 3321.94 | 3355.4900000000002 | 3376.55
 | 6.5622 | 6.9609 | 7.8127 | 9.49 | 11.1534 | 12.8037 | 16.1068 | 19.3879 | 25.9613 | 32.5304
ivyscript automated workflow:
Measure max IOPS (not shown)
Measure "baseline" service time at 1% of max IOPS
Use PID loop dynamic feedback control to measure IOPS for various multiples of baseline service time

## Slide 14: measure=IOPS, cooldown_by_wp=on
Chart: Seconds
Warmup IOPS | 34402 | 42682 | 46147 | 46135 | 46197 | 47208 | 9018 | 1836 | 802 | 8209 | 7929 | 213 | 10891 | 7723 | 2722 | 3181 | 3093 | 3856 | 2838 | 2084 | 2792 | 1881 | 3806 | 1846 | 3366 | 1522 | 3570 | 1212 | 7204 | 1245 | 2136 | 1484 | 2546 | 1447 | 2737 | 1667 | 2153 | 849 | 880 | 752 | 781
Measurement IOPS | 888 | 909 | 1085 | 832 | 906 | 1123 | 973 | 959 | 920 | 1070 | 1045 | 943 | 1083 | 954 | 1027 | 1130 | 1141 | 1081 | 1106 | 896 | 1028 | 1105 | 887 | 1037 | 874 | 959 | 936 | 782 | 1034 | 949 | 949 | 932 | 902 | 884 | 986 | 876
Stable measurement period identified by measure algorithm
Initial transient behaviour
cooldown_by_wp = on extends until WP is empty.
(WP data from cmd dev.)

## Slide 15: DFC on command device connector data
Chart: For parity group busy % = 10%, 20%, 30%, …
| 9.950800000000011E-2 | 0.19962099999999997 | 0.29997200000000035 | 0.40008000000000027 | 0.50149100000000002 | 0.60100600000000004 | 0.70207500000000045 | 0.80312099999999997 | 0.90364599999999995 | 0.95612600000000003 | 0.99374700000000005
 | 3612.13 | 7680.14 | 11794.7 | 17398.6 | 23119.2 | 30544.7 | 39590.5 | 52291.5 | 74647.2 | 98869.1 | 153015
Actually achieved PG busy %

## Slide 16: Fine-grained dynamic feedback control
Chart: 
| 10% busy | 20% busy | 30% busy | 40% busy
MPU0 | 12574.6 | 26557.2 | 42388.2 | 57959.5
MPU1 | 9852.86 | 20783.7 | 33109.1 | 45796.2
MPU2 | 11482.2 | 25159 | 40517.9 | 55810.4
MPU3 | 9474.12 | 20309.9 | 32416.3 | 44996.2
[CreateRollup] "MPU";
[Go!] "DFC=PID, focus_rollup=\"MPU\" …"
IOPS

## Slide 17: Service time histograms
Chart: Read Service Time at 90% of max IOPS
| 0.0x | 0.1x | 0.2x | 0.3x | 0.4x | 0.5x | 0.6x | 0.7x | 0.8x | 0.9x | 1.x | 2.x | 3.x | 4.x | 5.x | 6.x | 7.x | 8.x | 9.x | 10.x | 11.x | 12.x | 13.x | 14.x | 15.x | 16.x | 17.x | 18.x | 19.x | 2x. | 3x. | 4x. | 5x. | 6x. | 7x. | 8x. | 9x. | 1xx. | 2xx. | 3xx. | 4xx. | 5xx. | 6xx. | 7xx. | 8xx. | 9xx. | 1xxx. | 2xxx. | 3xxx. | 4xxx. | 5xxx. | 6xxx. | 7xxx. | 8xxx. | 9xxx. | 10000+
90% of max IOPS 100% read | 0.33 | 0.073333 | 0.0066667 | 0.0033333 | 0.0066667 | 1.07 | 11.8433 | 42.4867 | 85.5067 | 120.58 | 134.537 | 129.66 | 112.63 | 98.2333 | 87.17 | 73.7767 | 63.5733 | 55.0167 | 49.4233 | 43.66 | 38.8767 | 33.6067 | 31.0333 | 28.2633 | 169.49 | 70.3267 | 31.1833 | 14.57 | 7.3933 | 3.9867 | 1.9867 | 1.1033 | 1.4033 | 0.0066667
90% of max IOPS 75% read | 0.17209 | 0.054016 | 0.012048 | 0.0072289 | 0.0086345 | 0.0040161 | 0.0040161 | 0.0050201 | 0.0032129 | 0.38133 | 4.458 | 16.9014 | 34.7841 | 50.401 | 59.4129 | 61.2412 | 58.6414 | 55.2402 | 52.0253 | 48.0966 | 43.1629 | 38.3028 | 34.3253 | 30.3819 | 26.7347 | 23.8488 | 21.912 | 20.0799 | 133.534 | 69.7528 | 41.6735 | 27.49 | 18.756 | 13.254 | 9.4034 | 6.7781 | 17.851 | 1.206 | 0.11165 | 0.01245 | 0.0012048 | 0.0002008
90% of max IOPS 50% read | 0.14984 | 0.041042 | 0.0013029 | 0.0019544 | 0.0013029 | 0.00065147 | 0.25668 | 3.3974 | 12.0319 | 22.2313 | 30.1824 | 33.0762 | 31.5713 | 28.9596 | 27.1954 | 25.542 | 23.0873 | 20.6756 | 18.4365 | 16.7016 | 15.058 | 13.7687 | 12.7752 | 12.0072 | 11.1062 | 83.6156 | 49.8358 | 32.3433 | 22.129 | 15.5837 | 11.2899 | 8.1062 | 5.8234 | 15.602 | 1.0143 | 0.10749 | 0.011075 | 0.0019544 | 0.00065147
90% of max IOPS 25% read | 0.063535 | 0.029978 | 0.00022371 | 0.00022371 | 0.00022371 | 0.11723 | 1.6479 | 5.5586 | 10.1076 | 13.4311 | 14.6676 | 13.8065 | 12.4065 | 11.3633 | 10.3899 | 9.2723 | 8.1962 | 7.3461 | 6.7763 | 6.2924 | 5.9931 | 5.6796 | 5.4711 | 5.2074 | 41.3841 | 24.8418 | 14.9168 | 9.8926 | 6.8058 | 4.9157 | 3.5902 | 2.7982 | 9.317 | 1.0611 | 0.17673 | 0.029083 | 0.0071588 | 0.0011186 | 0.00044743 | 0.00022371
90% of max IOPS 0% read
Chart: Write Service Time at 90% of max IOPS
| 0.0x | 0.1x | 0.2x | 0.3x | 0.4x | 0.5x | 0.6x | 0.7x | 0.8x | 0.9x | 1.x | 2.x | 3.x | 4.x | 5.x | 6.x | 7.x | 8.x | 9.x | 10.x | 11.x | 12.x | 13.x | 14.x | 15.x | 16.x | 17.x | 18.x | 19.x | 2x. | 3x. | 4x. | 5x. | 6x. | 7x. | 8x. | 9x. | 1xx. | 2xx. | 3xx. | 4xx. | 5xx. | 6xx. | 7xx. | 8xx. | 9xx. | 1xxx. | 2xxx. | 3xxx. | 4xxx. | 5xxx. | 6xxx. | 7xxx. | 8xxx. | 9xxx. | 10000+
90% of max IOPS 100% read
90% of max IOPS 75% read | 47.4494 | 179.16 | 11.5934 | 9.2586 | 7.1843 | 5.0932 | 4.5394 | 4.3038 | 4.1203 | 33.9386 | 19.9825 | 8.7104 | 3.2034 | 0.89197 | 0.31245 | 0.11526 | 0.047189 | 0.016667 | 0.0054217 | 0.0034136 | 0.001004 | 0.0002008 | 0.0002008
90% of max IOPS 50% read | 101.851 | 476.814 | 12.8345 | 2.3127 | 1.63 | 1.1107 | 0.85994 | 0.62997 | 0.47622 | 3.2072 | 0.9114 | 0.36482 | 0.19935 | 0.087296 | 0.057329 | 0.033225 | 0.014332 | 0.009772 | 0.0065147 | 0.0052117 | 0.0045603 | 0.0026059 | 0.0026059 | 0.0013029 | 0.00065147 | 0.00065147 | 0.0032573 | 0.0032573 | 0.0039088
90% of max IOPS 25% read | 112.717 | 674.049 | 16.9043 | 2.7485 | 1.7251 | 1.2944 | 1.0412 | 0.75839 | 0.62595 | 3.7626 | 1.2631 | 0.83535 | 0.62327 | 0.46197 | 0.3519 | 0.28971 | 0.21342 | 0.16644 | 0.13356 | 0.10447 | 0.083893 | 0.070694 | 0.05906 | 0.043624 | 0.035794 | 0.030649 | 0.025503 | 0.02528 | 0.11767 | 0.040268 | 0.0217 | 0.014541 | 0.012528 | 0.00783 | 0.006264 | 0.0049217 | 0.028412 | 0.0051454
90% of max IOPS 0% read | 788.3 | 217.327 | 6.7667 | 2.2833 | 1.3567 | 1.0033 | 0.81667 | 0.65333 | 0.62667 | 2.84 | 0.20333 | 0.01

## Slide 18: Workloads can be placed within the LUN
Chart: Sequential MB/s by zone

## Slide 19: Ivy development status
August, 2016
  Internal HDS performance team user beta test in progress, including test of dedupe & compression support
  Released as open source.
  Demos available for all functionality.
  Support for HUS VM, VSP Gx00.
  Support for HUS100 series.

## Slide 20: Ivy futures
Some ideas:
  Repackage access to ivy engine via a RESTful API.
    Build CLI on RESTful API to enable programming ivy in Python or any other language
    Remove outer ivyscript programming layer wrapper, exposing ivy engine control statements as CLI commands.
  Develop VSP G1000 support
  Extend VSP Gx00 support
  Develop "auto gain control" feature for PID loop
  Transition to POSIX asynchronous I/O and port to other OS platforms.

## Slide 21: Thank You